## Slide 1
RESEARCH PROTOTYPE
Interactive eVTOL
Vertiport Siting &
Route Planning
A two-dimensional decision-support system integrating demand generation, spatial risk and cost modeling, K-means, genetic algorithms, A*, and RRT*.
Demand → Candidates → Optimized Sites → Routes
System Overview | English Presentation

## Slide 2
SYSTEM LOGIC
One continuous workflow links strategic siting to operational routing.
01
Urban Scenario
Generate weighted passenger demand, risk hotspots, and spatial cost fields.
→
02
Candidate Generation
Apply weighted K-means; cluster centers become candidate vertiports.
→
03
Siting Optimization
Use a genetic algorithm to balance coverage, safety, and cost.
→
04
Route Planning
Plan routes from selected vertiports to a fixed airport connection point.
→
05
Algorithm Comparison
Compare A* and RRT* through paths, search behavior, and quantitative metrics.
The same spatial fields and selected sites are reused across modules, preserving consistency between planning stages.

## Slide 3
MODULE 1 · SITING
The siting engine makes demand, risk, and cost trade-offs visible.
Demand model
Weighted Gaussian demand clusters approximate heterogeneous urban travel demand.
Candidate sites
Weighted K-means converts dispersed demand points into interpretable candidate locations.
GA objective
F = w₁·coverage − w₂·risk − w₃·cost
Interactive output
Users can change seeds, weights, cluster count, population size, and generations.

## Slide 4
OPTIMIZATION EVIDENCE
The GA exposes convergence instead of presenting a black-box answer.
What the user can inspect
01
Best fitness
Tracks the best solution found across generations.
02
Mean fitness
Shows population-level improvement and stability.
03
Site metrics
Coverage, risk, cost, and single-site score remain exportable.
04
Reproducibility
Random seeds allow repeatable experimental scenarios.
Result: an auditable optimization process suitable for thesis experiments and parameter-sensitivity studies.

## Slide 5
MODULE 2 · ROUTING
Selected vertiports become route origins to a fixed airport connector.
Shared edge-cost model
J = α·distance + β·risk + γ·cost
A*
Grid-based search
Open/closed lists, obstacle inflation, Euclidean or Manhattan heuristic.
RRT*
Continuous-space sampling
Goal bias, collision checking, neighborhood rewiring, optional smoothing.
Risk field
Risk-aware feasibility
High-risk cells become obstacles; remaining fields contribute to route cost.

## Slide 6
ALGORITHM COMPARISON
A* and RRT* are compared on both solution quality and search effort.
Evaluation dimensions
Path quality
Length, cumulative risk, cumulative cost, average risk
Safety
Minimum obstacle clearance
Performance
Runtime and explored/tree node count
Smoothness
Turn count and tortuosity
The interface automatically summarizes which algorithm is shortest, safest, and fastest under the current parameter set.

## Slide 7
RESEARCH VALUE
The system is designed as an experimental platform,
not a one-off visualization.
01
Interactive experimentation
Scenario seeds, demand structure, objective weights, and algorithm parameters can be changed without editing code.
02
Transparent methodology
Each intermediate stage is visible: fields, demand points, clusters, candidate sites, optimized sites, search trees, and final routes.
03
Extensible architecture
The modular Python structure supports real GIS data, multi-objective optimization, capacity constraints, and new planners.
Next step: replace synthetic fields with real urban demand, land-cost, airspace, and infrastructure datasets.